## Slide 1
Splash
Radiochemistry Platform

## Slide 2
Login

## Slide 3
Home
Manage my account
Manage system users
View and export log data
This option will be available in the AIR client.
Options only available to system administrators.
Allows users to change their password and personal information.
Watch the run that is currently in progress
This option will appear when another user is running the system.

## Slide 4
Select
(Sequences)
Sequences
Choose a sequence from this tab and use the buttons below to do one of the following:
View
Copy
Edit
Run
Delete
Create a new sequence from scratch.
Design note: we want it to be obvious which of the two tabs is selected.

## Slide 5
Select
(Run History)
9/21/2011 hsimpson FAC Synthesis 10.4% FAC
9/19/2011 hsimpson FAC Synthesis 14.7% FAC
9/16/2011 hsimpson FAC Synthesis Gasket fell off
Choose a past run from this tab and either view it or copy it to a saved sequence.

## Slide 6
Select Sequence
(Create)

## Slide 7
Select Sequence
(Copy)

## Slide 8
Select Sequence
(Delete)
Yes
No

## Slide 9
View Sequence
(Cassette)
Make this column wider to fit more descriptive text.
Click/tap an operation in the left panel to change the contents of the right panel.

## Slide 10
View Sequence
(Unit Operation)

## Slide 11
Edit Sequence
(Overview)
Click/tap an operation in the middle panel to change the contents of the right panel.
Set the operation parameters in the right panel.
Toolbox contains both unit operations.

## Slide 12
Edit Sequence
(Cassette)
Tap/click to enable or disable this cassette.
Tap/click to edit this reagent.

## Slide 13
Edit Sequence
(Cassette)
Tap/click to enable or disable this reagent.
Help strings describe each field.
Asterisks indicate required fields.
*
Name

## Slide 14
Edit Sequence
(Unit operation)
Server automatically fills in certain fields with default values.

## Slide 15
Edit Sequence
(Add, reorder
and delete)
Drag operation to trash can to delete.
Drag operation up or down to reorder.
Drag an operation from the toolbox and drop it in the sequence to add.

## Slide 16
Edit Sequence
(Validation)
!
!
Icons used to visually indicate validation errors.
A description of the validation error is displayed below the field.
The reagent field is required.

## Slide 17
Edit Sequence
(Validation)
!
!
The reagent field is required.
This sequence contains errors and cannot be run in its current form. Are you sure you want to go back before correcting these errors?
No
Yes
Validation errors will cause a warning when Back is clicked.

## Slide 18
Edit Sequence
(Validation)
!
!
The reagent field is required.
This sequence cannot be run because it contains errors.
OK
Validation errors will cause an error when Run is clicked.

## Slide 19
Run Sequence
(Start)

## Slide 20
Run Sequence
(Running)
The view will advance automatically with the run.
Adding Reagent
Adding MeCN to reactor 1 via delivery position 2. Using 5 PSI of nitrogen and delivering for 10 seconds.
Status: Delivering reagent
Reactor 1
Unit operations that have already passed are grayed out.
The current unit operation is progress is highlighted.
Pause After This Operation
Abort Run

## Slide 21
Run Sequence
(Running)
Adding Reagent
Adding MeCN to reactor 1 via delivery position 2. Using 5 PSI of nitrogen and delivering for 10 seconds.
Status: Delivering reagent
Reactor 1
The status of the unit operation.
Pause After This Operation
Abort Run
Push-in/out button will flag the system to pause after this unit operation.
Note: this is potentially confusing. Any ideas for a better control to toggle on and off?
Live video from the relevant reactor is shown.

## Slide 22
Run Sequence
(Timer)
Reacting
Reacting the contents of reactor 1 in position 2 at 160 C for 900 seconds. The vial is being stirred at 500 and will be cooled to 35 C when complete.
Status: Reacting, 3:14 remaining
Reactor 1
Pause After This Operation
Abort Run
Pause button will stop the timer and change to a Play button which will resume the timer.
Pause timer
Skip to next step
Complete button will cut the timer short.
Additional buttons will be present for unit operations that include a timer. Note: can we put these closer to the timer so their function is more intuitive? How to prevent accidentally clicking “Skip”? For example, Apple has two step controls for deleting things.

## Slide 23
Run Sequence
(Pause and Edit)
Continue Run
Abort Run
Unit operations that haven’t occurred yet can be edited.
Reagents and cassette positions that haven’t been used yet can be edited.
Unit operations that have already passed are grayed out and cannot be selected.

## Slide 24
Run Sequence
(Pause and Edit)
Continue Run
Abort Run
Any unit operation inserted before the current position will become the next unit operation.
The system will refuse to continue if there are any validation errors in the sequence.

## Slide 25
Run Sequence
(Abort)
Adding Reagent
Adding MeCN to reactor 1 via delivery position 2. Using 5 PSI of nitrogen and delivering for 10 seconds.
Reactor 1
Pause After This Operation
Abort
Are you sure you want to abort the sequence run? This operation cannot be undone.
No
Yes
The current run can be completely aborted.

## Slide 26
Run Sequence
(Complete)
Adding Reagent
Adding MeCN to reactor 1 via delivery position 2. Using 5 PSI of nitrogen and delivering for 10 seconds.
Status: Delivering reagent
Reactor 1
Pause After This Operation
Abort Run
OK
Sequence “FAC Synthesis” completed successfully.
Enter an optional comment for this run:
35.2% yield

## Slide 27
My Account
First:
Save
Homer
Cancel
Last:
Simpson
Change Password
User:
hsimpson
Role:
Administrator

## Slide 28
First:
Save
Homer
Cancel
Last:
Simpson
Change Password
User:
hsimpson
Role:
Administrator
My Account
(Password)
Enter your new password and verify:
Update
********
Cancel
Enter your current password:
********
********